## Slide 1: Wave direction prediction for O&M
Peter Mills
peter.mills@strath.ac.uk
B. Stephen, D. McMillan & I. Lazakis

## Slide 2: Outline
Introduction
Case Study
Prediction model
  Von Mises
  Copula
  Conditional probability
  Maximum likelihood estimation
Conclusions

## Slide 3: Introduction
O&M up to 30% of offshore wind lifetime costs [2]
Winter:
  Limited maintenance opportunities
  High energy yield
Aborted missions:
  fuel costs
Crew transfers: wave heights below 1.5 m [2]
[1] Yellow & Finch publishers. (2014). CTruk's Latest OWSV Impresses During Sea Trials | Yellow & Finch Publishers.
[2] I. A. Dinwoodie, D. McMillan, M. Revie, I. Lazakis, and Y. Dalgic, "Development of a combined operational and strategic decision support model for offshore wind," Energy Procedia, vol. 35, pp. 157-166, 2013.

## Slide 4: Wave direction
“Clear decision criteria must be in place for conditions under which transfers can take place. This is not as simple as setting a wave height limit; other important variables are: - the wave direction (relative to the vessel) …”
Energy Institute Working at height in the offshore wind industry
[1] Energy Institute. 2014, Good practice guideline Working at height in the offshore wind industry, Energy Institute, (London).

## Slide 5: Prediction
Historical data at Gabbard (origin site) & Southwold used for training
Prediction of wave directions at Gabbard given wave directions at Southwold
Case study location

## Slide 6: Directional data
Von Mises distributions are the assumed marginals for the wave directions
Notes: Not compatible with basic linear forecasting
Need circular distribution
Circular mean

## Slide 7: Von Mises distribution
Von Mises probability density function (pdf):
θ = wave direction (dominate peak)
μj = preferred direction
κj = concentration Parameter
I0 = Bessel function first kind order zero
preferred direction (μ)
f(κ)
[1] Probability Theory and Statistics (Introduction) Available: www.memrise.com

## Slide 8: Copula
Capture relation between sites
Sklar’s theorem:
where:
G = Gabbard & S = Southwold wave direction data
P(G,S) is the joint probability distribution
P(G) & P(S) are individual probability distributions
C[…,…] is the copula function
F(G)& H(S) are functions of wave directions
F & H denote the Von Mises cumulative distribution function

## Slide 9: Copula
Gaussian copula for a correlation coefficient (ρ) of 0.3 [1]
[1] M. B. Hassine. Introduction to Copulas [Online]. PowerPoint Presentation Available: http://slideplayer.com/slide/3270700/ [07/11/16]
Copula
  include dependencies
Gaussian Copula
  correlation
Maximum likelihood criterion
  select the most probable prediction

## Slide 10: Results
Actual
Copula
Prediction
Wave direction (deg)
Offsetting issue • Tracks

## Slide 11: Results
 | Circular mean absoluter error (degrees) | 
Limits (degrees) | Copula prediction | Persistence forecast (half hour ahead)
0 to 360 | 58.6 | 9.6
60 to 300 | 17.6 | 10.6
150 to 360 | 13.1 | 9.6
0 to 200 | 8.7 | 9.6

## Slide 12: Conclusions
Offsetting issue requiring further work
  Probability due multimodal data
Copula model captures additional information compared to other models
Copula allow inclusions of dependencies that traditional linear models do not
Model has flexibility to add other inputs
Prediction with absence of measurement point

## Slide 13: Future Work
Forecast – replace 2nd site with 1st site with time offset
Forecasting with multimodal distribution
Include more than 2 locations as forecast inputs
Inclusion of other variables
  Wind direction
  Marine current direction

## Slide 14
Questions ?
futurewind 2017 is sponsored by:
Organised by the Wind & Marine Energy Systems CDT

## Slide 15: Limitations
Transportation means | Maximum wave height (m) | Maximum wind speed (m/s)
Helicopter | 4 | 18
Crew Transfer Vessel | 1.5 | 25
Offshore Access Vessel | 2 | 25
Jack-up Vessel | 2.8 | 36
Leg-stabilised Vessel | 0.5 | 
[1] Dalgic, Y. Lazakis, I. & Turan, O. 2013. Vessel charter rate estimation for offshore wind O&M activities. Developments in Maritime Transportation and Exploitation of Sea Resources. CRC Press.
[2] Dalgic, Y. Lazakis, I. Dinwoodie, I. McMillan, D. & Revie, M. 2015a. Advanced logistics planning for offshore wind farm operation and maintenance activities. Ocean Engineering, 101: 211-226.
[3] Dalgic, Y. Lazakis, I. & Turan, O. 2015b. Investigation of Optimum Crew Transfer Vessel Fleet for Offshore Wind Farm Maintenance Operations. Wind Engineering, 39(1): 31-52.

## Slide 16: Conditional distribution predictor
Bayes theorem:
Substituting Sklar’s theorem for P(G,S) in Bayes theorem gives:
where:
G = Gabbard & S = Southwold wave direction data
P(G|S) is probability for Gabbard given Southwold wave direction
P(G,S) is the joint probability distribution
C[…,…] is the copula function
F & H denote the Von Mises cumulative distribution function

## Slide 18: Results
 | Circular mean absoluter error (degrees) |  | 
Limits (degrees) | Copula prediction | Copula forecast (half hour ahead) | Persistence forecast (half hour ahead)
0 to 360 | 58.6 | 22.6 | 9.6
60 to 300 | 17.6 | 30.0 | 10.6
150 to 360 | 13.1 | 9.9 | 9.6
0 to 200 | 8.7 | 2.7 | 9.6