## Slide 1: Control System Design of a Multi Rotor System
Author: Euan MacMahon
Email: euan.macmahon@strath.ac.uk
Supervisors: Bill Leithead, Peter Jamieson

## Slide 2: Motivation
Turbines increasing in size due to benefits of infrastructure and O & M
Scaling laws dictate that cost increases at a greater rate than energy capture
20 MW MRS shows potential 16% reduction in LCOE compared to two10MW single rotor turbines without including possible energy capture and O & M benefits[]
Fig 1: Vestas four rotor turbine
[1] Innwind.EU

## Slide 3: Design of MRS
InnWind design used
20 MW, 45 rotor design
No yaw actuator in order to reduce costs
Yawing implemented by varying thrust force on individual rotor and power conversion (RPC) systems
All modelling is done in Simulink

## Slide 4: Controller Design
Aggregate controller estimates to alter total yaw moment in order to reduce yaw error
Dispatch controller monitors state of individual turbines and works to optimise power
PAC controller used to reduce thrust of RPC systems
Double feedback loop needed
Initially thrust reduced equally for all rotors on one side

## Slide 5: Initial Results

## Slide 6: Optimisation of MRS
RPC systems further from the yaw axis generate greater torque for given reduction in power
RPC systems given ranking using rate of change of torque with pitch
Highest ranked RPC system will reduce thrust as much as possible to a safe limit
Any remaining from aggregate controller input to next highest ranked RPC system
8 rotor design used for initial testing

## Slide 7: PAC and Supervisory Control
Developed at Strathclyde the PAC wraps around FEC in order to change operating point
Safety limits needed to prevent operation in unsafe region
Flags to indicate region of operation
Limits on requested power of -30kW, -20kW and -15kW for green, amber and red regions respectively

## Slide 8: Example of Distribution of
Blue line represents power reduction requested from aggregate controller
RPC system is ranked at 50 seconds and so all assigned there initially
then exceeds safe limit for RPC system so power distributed to second highest ranked rotor (rotor )

## Slide 9: In depth look at distribution
At 66 seconds RPC system returns an amber flag
At 74 seconds a ranking swap occurs. RPC system becomes the second ranked rotor
At 77 seconds RPC system switches back to green however at 78 seconds it reverts back to amber

## Slide 10: Future Work
Implement optimisation technique to 45 rotor MRS
Analyse system with rotors removed to simulate rotor failure
Model floating platform and design control technique for stabilisation
Combine stabilisation and yawing

## Slide 11
Questions ?
futurewind 2017 is sponsored by:
Organised by the Wind & Marine Energy Systems CDT